DISK: MASTER TRIPLE DENSITY			2 June 1984
FILE: SERIAL#.DOC
:
PURPOSE: TO DEMONSTRATE THE PROCEDURE FOR CORRECTING CPM SERIAL NUMBERS.

WHEN GENERATING A NEW VERSION OF THE SYSTEM IMAGE, THE CPM SERIAL NUMBERS
OF THE SYSTEM IMAGE ON THE SYSTEM TRACKS AND THE ROUTINE MOVCPM.COM MUST
BE IN AGREEMENT.

THE CPM SERIAL NUMBER IS COMPOSED OF 6 BYTES:
				BYTE #.
1           2           3           4           5           6
OEM REG #   16H=2.2CPM  CPM REV #   |---------SN-------------|


THE SERIAL NUMBER APPEARS TWICE IN MOVCPM.COM, AT LOCATIONS:
	0D28H   AND  1200H

DDT MOVCPM.COM
-D0D28		=> 6 BYTES REG # IN CCP
-S0D2B
0D2B XX N1   1ST DIGIT OF SN.
0D2C YY N2   2ND DIGIT
0D2D ZZ N3   3RD DIGIT  (NOTE: YOUR SN IS GIVEN IN DECIMAL AND MUST BE
0D2E ## .	         CONVERTED TO HEX.)
-D1200          => 6 BYTES REG # IN BDOS
-S1200
1200 XX N1
1201 YY N2
1202 ZZ N3
1203 ## .

THE SERIAL NUMBER APPEARS TWICE ON THE SYSTEM TRACK FOR SINGLE DENSITY.

NDUMP T 0 S 8 EDIT		BYTES 28 29 2A 2B 2C 2D  (CCP SN)
 EDIT - 0028
0028 UU N1
0029 VV N2
002A WW N3
002B XX N4
002C YY N5
002D ZZ N6
002E ## .
 EDIT - WRITE		(WRITE CHANGES TO SYSTEM TRACKS)

NDUMP T 0 S 18 EDIT		BYTES 1 2 3 4 5 6   (BDOS SN)
 EDIT - 1

ETC.		(REPEAT AS ABOVE)