V B I O S 2 2 . D O C
		   --------------------------------------
	
	
	     Documentation file for a 3.5" Versafloppy BIOS.  By

  		              Ramon F. Gandia
		        P.O. Box 970, Nome, AK 99762
			       27 April 1995
	

		This material is for implementing 3.5" disk drives on
	a VERSAFLOPPY II controller.  The BIOS is short and sweet; has
	decent error recovery and retries, and appears to be reliable
	and stable.  The 3.5" disks are formatted to 128 byte sectors,
	26 sectors per track and 80 (77 usable) tracks per disk.
	Single sided, BUT double density.  This disk format emulates
	the standard 8" floppy and was thus chosen.

		Notice that the BIOS is in two parts. The main part is
	intended as ROM-resident, but for test purposes is in RAM at
	A800h.  It remains in that location regardless of the size
	CP/M you make for the versafloppy (up to about a 40K system).
	It was chosen to be at A800 for a very good reason.  If you
	have a 56K or larger cp/m system, you can bring this BIOS &
	system to life under it.  Your DDT will load between my A800
	BIOS code and your DDT and will not be wiped out. Therefore,
	you can have your cp/m, your DDT and my BIOS coexisting with
	each other.  This makes development and experimenting easy. If
	and when you decide to burn the BIOS into a ROM, I suggest you
	reassemble it for a much higher location.  F800 in my case....

		Disks are formatted using 22-DISK, but blank formatted
	ones are included for your experimentation.  22-DISK is a VERY
	SLOW formatter!

		Appendix I to this file has the neccessary information
	to add this particular format to your copy of 22-DISK.  My own
	format program works, but has no verify after write.  Although
	it appears to work, I am scared to death of it and won't
	release it for now.
    
                         --------------------
 
	A. Material included:

	4 Identical 3.5" disks, with cp/m system
	4 Formatted but blank disks (cp/m format) for experiments
	2 Identical 3.5" disks, IBM 720K with files

        B. Files on IBM disk:

	VBIOS22.Z80	-     Source code for PROM portion of BIOS
	IBIOS22.Z80	-     Source code for disk resident portion
			           of BIOS (Jump table & disk tables)
	VBOOT22.z80	-     Source code for BOOT (for sector 1,
				   track 0 of cp/m disk)
	SYSGEN22.Z80	-     Source code for customized SYSGEN.
	VBIOS22.DOC     -     This file.
	ZASMB.Z80	-     Modified source code for ZASMB (mods
				   were to eliminate display-specific
				   code.  Now is generalized TTY)
	ZASMB.CPM	-     Object code of above.  Use with 22-NICE.
	ZASMB.COM	-     Attach file to run above under 22NICE
			      (GENCOM ZASMB dis=ADM)
	ZASMB.DOC	-     Documentation on ZASMB.
        ZASMBREA.DME    -     My notes on ZASMB.

	C.  Files on CP/M disk:

	PIP.COM		-     Standard cp/m utility
	DDT.COM		-        "      "      "
	STAT.COM	-	 "      "      "

	VBIOS22.Z80	-     See above
	VBOOT22.Z80     -      "    "
	IBIOS22.Z80     -      "    "
	SYSGEN22.Z80    -      "    "

	VBIOS22.COM	-	object code
	VBOOT22.COM     -         "     "
	IBIOS22.COM     -         "     "
	SYSGEN22.COM    -         "     "
	CPMV40.COM      -       System image

	ZASMB.COM	-	  "     "

	D.  Bringing up the system.

	My computer has a PROM monitor with the following routines:
	
		CONST -  console status
		CONIN -  console input
		CONOT -  console output
		LIST  -  list output
		READER-  reader input
		PUNCH -  punch output
		LISTST-  list status
		ZMSG  -  routine to display an ASCIIZ message.
			 On entry (DE) points to start of the
	                 message, which must end in a 0.  The
			 routine puts the message on screen and
			 returns.
	
	I slightly altered the copies of VBIOS22 and VBOOT22
	to eliminate the need for ZMSG.  You will see my code
	commented out, and a new routine called QMSG at the
	end of the BIOS that does the same thing.  Both work
	in my system.  
	
	You should bring up the file VBIOS22.Z80 on your editor
	and modify the jump table so it points at the entry points
	of your system.
	
	Assemble the above using ZASMB.
	
	A>ZASMB VBIOS22  <cr>        (.COM file generated directly)
	
	If you want the assembler to generate a .LST file, eliminate
	the semicolon in front of the LIST ON directive at the top of
	the file. Be sure "list on" is NOT on the first column!
	
	Now you are almost on the air.

	Plug in your Versafloppy card, plug in your drives using a
	straight thru ribbon cable (not the PC variety with twist at
	the end.  One of your drives should be jumpered DS0 and the
	other DS1.

	With your regular cp/m system booted, bring in the BIOS as
	follows:

	A>DDT VBIOS22.COM     (bring in BIOS code)
	  _gA800              (jmp to cold boot)

	My system should now sign on.
	
	(Alternatively, you could load VBIOS22.COM with your DDT and
	then patch into the JUMP table directly at A800.  This would
	save you from having to mess with ZASMB).

	E.  Coming soon.

	Possibly a FORMAT program, but this will probably await
	later releases of the BIOS.

	Planned is an all-new BIOS implementing 1.44MB diskettes with
	deblocked 512 byte sectors.  Scheduled for late summer or fall
	of 1995.

			A P P E N D I X    I

			   Using 22-DISK
	
	
	You must edit your CPMDISKS.DEF file in 22-DISK to add this
	format to it.

	First, copy your present file to something else.

	C:>copy CPMDISKS.DEF CPMLULU.DEF

	Second, you must make a straight ASCII file out of it.

	C:>STRIPIDX cpmdisks.def

		Third, bring it into your word processor.  Make sure
	you are in a straight text mode and not some mode that puts in
	extraneous characters!  Go down the list and insert the
	following definition in its correct alphabetical position:

BEGIN VER2 Versafloppy II 3.5" 128/26/77 ALTAIR
DENSITY MFM ,LOW
CYLINDERS 80 SIDES 1 SECTORS 26,128
SIDE1 0 1,7,13,19,25,5,11,17,23,3,9,15,21,2,8,14,20,26,6,12,18,24,4,10,16,22
BSH 3 BLM 7 EXM 0 DSM 242 DRM 63 AL0 0C0H AL1 0 OFS 2
END

	22-DISK is very fussy, and the above must be typed EXACTLY as
	shown, notice the space between MFM and the comma, for
	instance.  The line containing the sector translate table must
	be all one line; cannot be split into two lines, etc.

	Once you have it all typed in, exit your editor, then:

	C:>GENINDEX cpmdisks.def

	Then try it.  Expect over 5 minutes to format a floppy!

			A P P E N D I X     I I

			  Quirks and features

	1.  Using 1.44MB disks or drives.  My drives are the 1.44
	    variety, TEAC FD-235HF.  These are best, but the older,
	    cheaper, 720K variety should also work.  HOWEVER, you MUST
	    use 720K disks.  If you have none, put a write protect tab
	    over the 1.44 MB diskette I.D. hole (the one on the right
	    as you insert the disk into the drive) to fool the drive
	    into thinking it is a 720K disk.  If you don't do that,
	    22-DISK will complain, and the end result will be a crash.
	    America On Line has sent everybody 1.44 disks, and I used
	    those for development, with the tab covering the I.D.
	    hole.

	2.  After the BIOS first accesses a disk, the drive light will
	    remain on until another disk is selected.  To correct this
	    without a watchdog timer and interrupts will entail a bit
	    of code to reside in CONIN.  This is hardware dependent,
	    and I left it out for now.	(Although I have this routine
	    working on my system).

	3.  The ZASMB assembler has a bug in that it won't assemble
	    .COM files ORGed below 0100h.  This is why VBOOT22 is
	    ORGed at 0100 instead of the more sensible 0080h.


	               A P P E N D I X     I I I
	
			 Inter-CP/M gymnastics
	
	If you haven't recently developed a cp/m system under another
	one, the following may save you a bit of work....  HOWEVER,
	be advised, changes to VBIOS22 will NOT require the following
	chinese circus.  VBIOS22 does not reside on the disk system
	image.  It is here in case you change the IBIOS22 or the
	VBOOT22 routines.
    
                        System Generation Under 
    			     Another CP/M
    
	[for purposes of clarity, the parent system will be 0A> and
	the child system 1A>.
    
        0A>MOVCPM 40 *         (generate 40K cp/m image, MDS800 bios?)
        0A>SAVE 35 CPM40.COM
        0A>DDT VBIOS22.COM     (bring in my VBIOS22)
    	_iIBIOS22.COM	       (Also bring in my IBIOS22)
    	_R
    
    	_LA800		   (Look around, make sure BIOS is ok)
    	_L9A00		   (Make sure IBIOS22 is there)
    	_F9AD1,9AFF,00	   (Clean up junk)
        _ICPM40.COM	   (Bring in cp/m and junk BIOS)
        _R
    	_IVBOOT22.COM	   (Bring in VBOOT22)
        _R
    	_M0100,017F,0900   (Move VBOOT22 to proper patch place)
        _M9A00,9ADF,1F80   (Ditto for the IBIOS22)
        _F0100,08FF,00     (Clean up junk)
    	_F2051,5000,00     (Clean up more junk)
        _L900		   (Look around, make sure all ok)
        _L1F80             (Ditto.  Make sure a RET is at 2050)
        _L980		   (Make sure cp/m itself starts at 980)
        _G0		   (Exit to the prompt)
	
        0A>SAVE 32 CPMV40.COM  (A new system image file, shorter) 
	
        0A)DDT
    	_F0100,5000,00     (ensure clean work space)
        _ICPMV40.COM
        _R		   (bring in the image)
        _GA800             (jump into versafloppy system)
        ALTAIR...V 2.2   40K CP/M.
	
        1A>SAVE 32 CPMV40.COM  (Notice this save is to 3.5" disk)
    
	(Now a good cpmv40 image resides in your 3.5" disk...)
	
	(Cleaning up "junk" may not sound important, but I've
	discovered that if you don't, the system can get buggy or not
	work at all.  Keep only the image between 900h and 2050 and be
	sure to zero everything else before SAVEing or SYSGENing. 
	Caveat Emptor!).
    
    		               SYSGEN
    
	To generate the system, you have TWO alternative sources.
	From disk or from memory.  The memory method is:
    
	First, have a good CPMV40.COM ready to load.
    
        1A>DDT CPMV40.COM       (Bring in the image - suggest you
                                 look it over and make sure it as
                                 expected).
       _ISYSGEN22.COM           (Bring in SYSGEN22)
       _R
       _G0100		        (Execute it.  From here on, it is
                                 just as shown below for disk-disk)
    
	                - disk to disk method -
	
       1A>SYSGEN22
    	
       3.5-inch Versafloppy II SYSGEN v 2.2
       SOURCE drive letter or <cr> to SKIP   (answer A or <cr> for mem)
            SOURCE already in memory         (assuming a <cr>
       DESTINATION drive letter or <cr> to QUIT   (enter B or whatever)
       
       System generation complete
    
       1A>
    
       (Note that SYSGEN22 uses VBIOS22, the latter must be resident).
    
    			    SYSTEM TO SYSTEM COPY
    
	My system boots at 0080H, therefore it does not ruin the TPA.
	It may not be too clear from the above that copies can be made
	of files from disk to disk, up to the size of the TPA.  Here
	is how:
    
        0A>DDT yourfile.xyz
        NEXT   PC
        3600   0100     <------- for example
    
                    3600 minus 0100 is 3500.  Convert to decimal
                         3 times 16 = 48
                    	 5 times  1 =  5
                                    ------
    				      53  total pages
    
       _GA800       (Boot up versafloppy)
 
       ALTAIR...V 2.2   40K CP/M.
	
       1A>SAVE 53 yourfile.xyz   (This saves your file to 3.5" disk)
    
                             LITTLE HELP AIDS
    
	I have a file in the 3.5" disk which boots my older cp/m, and
	a file in the older cp/m that boots up my versafloppy. These
	are very short and simple, just a jump, really, to the other
	system's boot.  The file to go into the 3.5 disk is up to you
	to make, but for the other way around it is:
    
        0A>DDT
    	_A0100
        0100   jmp a800
        0103    <cr>
        _g0
	
        0A>SAVE 1 BOOTVER.COM
	
			  PHYSICAL MODIFICATIONS
	
		The Versafloppy II controller will work as-is with the
	above BIOS; however, it contains what I consider a design flaw
	in the RESET circuit.
	
		As shipped, the board resets ONLY on *POC
	(power-on-clear).  In my Altair, *POC is only asserted during
	power up.  Activating the reset switch to either the RESET or
	the EXT CLR position does not reset the controller.  While
	experimenting, you will often find that the controller locks
	up on a wait state.  There is no way out of this except to
	reset the controller.... If you must do this by powering 
	down the computer, your memory will be wiped out, and lord
	knows what else.
	
		What I did to mine was to move the reset line from the
	*POC pin (99) to the *EXT CLR pin (54).  If your computer does
	not have a separate *EXT CLR switch as mine does, move the
	signal to *RESET pin (75), which will accomplish the same
	thing but is not quite as flexible.
	
		To do this, take a sharp pointed tool and cut the
	trace leading away from pin 99.  It is the only trace going
	there.  Locate pin 54 (or 75).  Notice that the fingers have
	no traces going to them.  Solder a small piece of wire from
	the very top end of pin 54 (or 75) to the trace that used to
	go to pin 99.  Rather than have the wire span the whole board,
	you could follow the old pin 99 trace about halfway on the
	board and solder to it there.  When you are satisfied that all
	works to your satisfaction, a little epoxy or hot melt glue
	will prevent the wire from getting snagged.
	
		Make the pin 54 or 75 connection at the very, very
	top end of the finger, or the solder blob will not allow the
	card to go into the S-100 backplane.  In my system there is
	about 1/8-inch to do this.
	
		This is a very worthwhile modification that will
	prevent a LOT of hair pulling!  However, if you have a working
	BIOS to begin with, it should not be neccesary.
	
	
	  			- 30 -