THe step rates of floppy drives (and other features) are controlled by
a set of tables in the DDBIOS ROM. Look at the listings for details.
THere are tables for the following drives at these locations:
	8" sd @ F03F
	8" DD @ F048
	8" DD/256 byte sectors @ F051
	5" SD @ F05A
	5" DD @ F063

The table format is
	DB	xx	;sectors per track
	DB	xx	;tracks per side
	DB	xx	;index header  gap for formatting
	DB	xx	;gap 1
	DB	xx	;gap 2
	DB	xx	;gap 3
	DB	xx	;restore command for floppy chip
	DB	xx	;seek/no verify command
	DB	xx	;seek/verify command

The last three commands have imbedded within them two bits that control
the step rate of the drive as follows:

	bit 1   bit 0		8"drive		5"drive
	0	0		3ms		6ms
	0	1		6ms		12ms
	1	0		10ms		20ms
	1	1		15ms		30ms

Change these bits in the ROM (by burning another ROM!) to change the
drive step rates. The two versions of the PROMS on this disk have
the fastest and slowest step rates for the 8" drives within them.